Breadboard prototype

 Sensors

Sensor ID	Other names	Sensor Name	Voltage	I2C
BH1750		Light	3-5	0x23
MPR121		Cap Touch	3.3
BME280	BMP280	Temp Press Humid	5	0x76
HW246	QMC5883L GY121	Magnetic Field	3-5	0x0D

Tested all the sensors using code generated via chatGPT and all seemed to work as desired. The capacitive touch sensor was probably the most tricky. 1) because it requires transferring the logic from 3.3V to 5V (If i wanted all the sensors to remain on the same line). And 2) it was a bit finicky to calibrate.
Important Arduino code
3 data streams
The following code is intended to output temperature, lux, and MagX

#include <Wire.h> / #include <Adafruit_BME280.h> / #include <Adafruit_Sensor.h> / #include <BH1750.h> / #include <QMC5883LCompass.h> / // Sensor objects / Adafruit_BME280 bme; // BME280 environmental sensor / BH1750 lightMeter; // BH1750 light sensor / QMC5883LCompass mag; // QMC5883L magnetometer / void setup() { / Serial.begin(9600); / Wire.begin(); / // Initialize BME280 / if (!bme.begin(0x76)) { / Serial.println("BME280 not found!"); / } / // Initialize BH1750 / if (!lightMeter.begin(BH1750::CONTINUOUS_HIGH_RES_MODE)) { / Serial.println("BH1750 not found!"); / } / // Initialize QMC5883L / mag.init(); // NOTE: no return value / } / void loop() { / // Read temperature / float tempC = bme.readTemperature(); / // Read light level / float lux = lightMeter.readLightLevel(); / // Read magnetometer / mag.read(); / int magX = mag.getX(); // choose X-axis only / // Print values in a clean PD-friendly packet / Serial.print("TEMP "); Serial.print(tempC); / Serial.print(" LIGHT "); Serial.print(lux); / Serial.print(" MAGX "); Serial.println(magX); / delay(50); / }

Arduino Libraries:
QMC5883LCompass

Sensor Specifications:
BME280
Specification:
Model: BME280
Interface: I2C and SPI
Supply Voltage: 5V
Operating range: -40˚C to +85˚C
Rel. humidity: 300-1100 hPa
Humidity Range: 0 - 100 %

Features:
1. Digital interface I2C (up to 3.4 MHz) and SPI (3 and 4 wire, up to 10 MHz)
2. Supply voltage VDD main supply voltage range: 1.71 V to 3.6 V, VDDIO interface voltage range: 1.2 V to 3.6 V
3. Current consumption:
1.8 uA @ 1 Hz humidity and temperature
2.8 uA @ 1 Hz pressure and temperature
3.6 uA @ 1 Hz humidity, pressure and temperature
0.1 uA in sleep mode

Package Inlcuding:
4 X GY-BME280-5V Sensor
4 X 4P Straight Pin Header
Pure data patch screenshots
Simple com7 serial read patch

Puredata externals
- eimlib
- comport